## Slide 1: Presented by:
David J. Meyers
Rinke Noonan
St. Cloud
Dennis Pederson, LS
Bogart, Pederson & Associates
Becker, MN

## Slide 2: DEALING WITH THE “BAD” METES & BOUNDS
WHY IT IS A PROBLEM AND HOW TO FIX IT

## Slide 3
Some of the illustrations and comments are courtesy of:
Fant, Freeman & Madson
On
Writing Land Descriptions
A publication of the Minnesota Society of Professional Surveyors
2011

## Slide 4
Two types of surveys
  Original

## Slide 5
  Creates the boundary.
  Perpetuates the boundary using monuments.
  Original monuments have no error. See: Minnesota Title Standards, Guidelines for Legal Descriptions No. 2.1 and 3.1.

## Slide 6
  B. Creates the boundary.
    Follow in the footsteps of original surveyor.
    The definition of a legally sufficient real property description is one that can be located on the ground by a surveyor. See: Minnesota Title Standards, Guidelines for Legal Descriptions No. 1.1

## Slide 7
Types of Metes & Bounds Descriptions – Basics
  Elements of Metes & Bounds Walkaround Description

## Slide 8
    Caption (or heading) (where is it) – The greater tract containing the parcel to be described.
    Examples:
        The Northwest Quarter of the Southeast Quarter of Section 16, Township 35, Range 30
        Lot 1, Block 1, Pearl Place, Pembina County, Minnesota

## Slide 9
  B. Body of description – The surveyor’s “set of instructions”

## Slide 10
    Point of commencement
        Example: Commencing at the Northeast Corner of the Northwest Quarter of the Southeast Quarter of Section 16, Township 35, Range 30, Sherburne County, Minnesota.

## Slide 11
    2. Point of Beginning
        Example: Thence along the North line of said Northwest Quarter of the Southeast Quarter 660 feet to the actual Point of Beginning of the land to be described.

## Slide 12
      3. Basis of Bearing
        Example: On an assumed bearing of 89° 16’ 42” along said line.

## Slide 13
4. Qualifying Clause – May modify or take something away
        Example: Except the south 330 feet thereof.

## Slide 14
b. Sometimes a qualifying clause is meaningless.
    “Commencing at the NW corner of said Section 25; thence South 30 rods to the intersection of a road leading from the county road at or near Charles Magnuson’s place in Sunrise City…” See: Mattson Ridge LLC v. Clear Rock Title, LLP, 824 NW2d 622 (Minn. 2012).

## Slide 15
5. Augmenting Clause
        Example: Together with an easement over…
        Example: Subject to an easement over…

## Slide 16
Types of Metes & Bounds Descriptions
  Bounds (or “Bounded by”)
    Example: That part of the Northwest Quarter lying southerly of the North 330 feet thereof, lying westerly of the centerline of County Road No. 2 and lying easterly of the meander river

## Slide 17
  Division line description
      Never assume that a platted lot is set to true North/South or East/West.

## Slide 19
  Linear description
      East 1,000 feet of…
      As measured at right angles…
      As measured along the ___ and ____ sides thereof.

## Slide 22
  Proportionate “of” Description
      East one-third of…
      East one-third by area…

## Slide 24
  Area Description
      Northerly 10.00 acres of…

## Slide 26
  Strip Description
  Curve Recitals

## Slide 27
  Azimuth - Direction Angles

## Slide 29
Public Land Survey System
  See www.mngeostate.glo OR www.glorecords.blm.gov

## Slide 31
  Eight Corners in a section.
    Subdivided into Quarters, Quarter-Quarters…

## Slide 32
Eight Government corners were set on each section. The center of section was calculated.

## Slide 34
The problem today is locating the original Government corners.
The cardinal rule is that the section corners are where they were placed by the government surveyor.

## Slide 35
  Divisions of Aliquot Parts
      Example: all in the Northwest Quarter of the Northwest Quarter;

## Slide 36
The East 80 acres ≠ the East 1320 feet ≠ East Half
          Never mix these descriptions

## Slide 37
  Aliquot Parts: All parts comprise the whole section.

## Slide 39
    The Northwest Quarter of the Northeast Quarter
    The East 1000 feet
    The South 1200 feet of the West 1200

## Slide 40
    NOTE: Rules governing the subdivision of sections have no application to the subdivision of land in a municipal plat of land. See: Minn. Stat. Chap. 505; Lavis v. Wilcox, 116 Minn. 187, 133 NW 563 (1911)

## Slide 41
Government Lots

## Slide 43
  West and north Tier of Township in Minnesota in both the 4th Principal Meridian (generally East of the Mississippi) or 5th Principal Meridian (generally West of the Mississippi).

## Slide 44
  Lakes and Rivers See: Minnesota Title Standards, Guidelines for Legal Descriptions No. 9

## Slide 45
    Meandered
    Non-meandered

## Slide 46
Problem Descriptions

## Slide 47
  The East 22 acres of a government lot

## Slide 49
  The point of commencement or point of beginning is on a lakeshore.

## Slide 50
  The North or South Half of a platted lot.

## Slide 52
  A cardinal direction, such as: South.

## Slide 57
  Area descriptions.

## Slide 58
  Gaps and Overlaps.
    With adjoining descriptions
    With occupation lines of long standing

## Slide 59
  Roads as boundary See: Minnesota Title Standards, Guidelines for Legal Descriptions No. 11

## Slide 60
Elements of a “Bad” Description:
  Ambiguity
  Patent – Defective on its face
  Latent – Defect discovered in the field
  Time Factors
    “Old” descriptions not fitting “new” conditions

## Slide 61
  Occupation/lines of possession not consistent with description
  Effect of MTA – 40-year Rule – Minn. Stat. §541.051
  Retracement issues with historic deeds

## Slide 62
Fixes

## Slide 63
  What doesn’t work.
    Boundary Agreement See: Slindee v. Fritch Investment, LLC, 760 NW2d 903 (Minn. App. 2009).
    Lawyer drafting a legal description

## Slide 64
  What may work.
    Deed exchange – IF a survey is also recorded

## Slide 65
    Quiet Title action – IF a survey is also recorded
      Note: Auditor must enter the Judgment in the transfer records. Minn. Stat. §559.23

## Slide 66
    Torrens Registration – IF a survey is also recorded
      Registering title alone does not register the boundary. See: Ruikke v. Nall, 798 NW2d 806 (Minn. App. 2011); Minneapolis & St. Louis Ry. Co. vs. Ellsworth, 237 Minn. 439, 54 NW2d 800 (1952); Minn. Stat. §508.671

## Slide 67
  What works.
    Torrens registration with judicial landmarks – See: Minn. Stat. §§508.06, 508.671, 559.25
    Quiet Title with judicial landmarks – See: Minn. Stat. §§559.23, 559.25
    Boundary Commission with judicial landmarks - See: Minn. Stat. §§465.79, 559.25

## Slide 68: Sources:
Minnesota Title Standards, Guidelines for Legal Descriptions and Survey Matters
Fant, Freeman and Madson – Writing Land Descriptions, Minnesota Society of Professional Surveyors
Fant, Freeman and Madson – Report 4, Metes and Bounds Descriptions, Minnesota Society of Professional Surveyors (Revised 1990) Out of Print